BCPL (Handler) Startup Magic and other things that shouldn't be documented...
-----------------------------------------------------------------------------
                © 1999 THOR-Software. Read the licence at the end!

$VER: BPCLMagic 1.0 (15.9.99)

    Abstract:
        This document describes the startup logic of the dos.library
        for BCPL-type handlers, using a GlobVec entry 0 or -3 in its 
        mountlist.

In this doc, tradenames and trademarks of some companies and products have
been used, and no such uses are intended to convey endorsement of or other
affiliations with the documentation.
____________________________________________________________________________

NOTE THAT ALL THIS INFORMATION IS OBSOLETE, NO NEW CODE SHOULD DEPEND ON
THIS *INTERNAL INFORMATION*. THE DOS BCPL HANDLING IS CLEARLY OBSOLETE AND
WILL BE MOST LIKELY REMOVED IN A FUTURE EDITION OF THE AMIGAOS.
____________________________________________________________________________

Thanks to Stephan Rupprecht for his Port-Handler and the interesting talk
that gave the impact of writing this.

Thanks to Ralph Babel for proof-reading this guide, and for some comments
and corrections.
____________________________________________________________________________

i)    What is this about?

Device handlers of the dos.library, the programs you find in L:, can be 
written either in C, Assembly,... or BCPL. BCPL programs require, due to
the logic of this language, special support from the Os, namely, the Os
has to build a so-called "global vector", containing handler global data
and function pointers to global BCPL procedures. Whether a handler requires
this special threatment is determinated by the "GlobVec" entry in the mount
list. If this entry is 0 or -3, then the code is recognized as BCPL code, if
it is -1 or -2, the "usual" startup code is run.

NOTE THAT IT IS LIKELY THAT THE BCPL STARTUP MAGIC WILL BE REMOVED IN 
FUTURE EDITIONS OF THE AMIGAOS.


ii) The "usual" startup code.

If the GlobVec entry in the mount list is -1 or -2, the handler code will
be run at the first byte of the first hunk of the binary. The dos library
will sent a startup message to the process port of the handler process,
which contains information for the handler where its "DosList" structure
is found. The startup message encodes a standard "DosPacket" structure
in the same way as all other packets sent to handlers: The pointer to
the DosPacket is found in the mn_Node.ln_Name pointer of the message.

The following entries in the DosPacket exit:


dp_Arg1:            This is a BCPL pointer to a BSTR containing the
                    device name.

dp_Arg2:            Contains the value found in the dol_Startup field
                    of the DosList. This information is handler specific,
                    but a well-accepted standard exist for filing systems.
                    It is documented in [1], for example.

dp_Arg3:            A BPTR to the DosList structure of the handler. In
                    case the dos library should launch a process for each
                    file to be opened, leave the dol_Task field NULL.
                    Otherwise, fill this field with a pointer to the
                    process message port of your handler.

dp_Arg4:            This field should be set to an alternative message port
                    in case you don't want to get incoming packets thru the
                    process message port.
                    (Documented in [1], untested by the author.)

The difference between a GlobVec of -1 or -2 is that the device list is
locked *exclusively* until the startup message is replied, but in the second
case only a shared lock is applied.

        *NOTE THAT USING THIS STARTUP MECHANISM IS RECOMMENDED*



iii) The BCPL startup code.

THIS STARTUP MECHANISM IS OBSOLETE. DO NOT USE IT, YOU DON'T GET *ANY*
ADVANTAGE BY USING THIS OBSOLETE MECHANISM. THE ONLY JUSTIFICATION FOR 
THIS STARTUP MECHANISM IS THAT IT MUST BE USED WHEN REPLACING OLD CBM
HANDLERS THAT STILL MAKE USE OF BCPL. These are currently the ram handler,
(RAM:), the port handler (PRT: SER: and PAR:) and some ROM-mounted filing
systems like DF0: and DF1:.

In case you want to replace these system handlers, only *ONE* BCPL GlobVec
entry must be re-defined, namely the startup vector #1 at offset +4, since
this is the vector the dos library uses to run your code. Unlike the "usual"
startup code, the dos.library will have removed the startup message already
for you, and will pass in a BPTR to the DosPacket as first BCPL argument in
register d1. Much more pre-defined global vectors exist and will be filled
in by the DOS on startup, but I leave them undocumented as all the function
pointers can be found as library entries in the dos.library anyways.

The BCPL startup code of the dos library reads the FIRST longword of each
of the hunks in the binary. Hence, even the first byte of the first hunk
is NO LONGER executable code. This long word contains the length of BCPL
segments in long words - which need not to be identical of the segment 
length stored in the hunk structure, it could be shorter. Hence, this is 
a long word offset, counted from the start of the segment up to the end of 
the BCPL segment part. Since this is the place where the GlobVec init data 
is stored, this offset counts the number of longs up to the end of the 
setup table. Graphically,


                +-------------------------------+
Segment - 4     | length of segment + 4         |
                +-------------------------------+
Segment - 0     | BPTR to the next offset       | <-- BPTR to this is returned
                |                               |      by LoadSeg()
                +-------------------------------+
Segment + 4     | longword offset as # of       |
                | from SegOffset - 0            |
                +-------------------------------+
                |                               |
                : GlobVec setup data, see       :
                : below                         :            ^
                |                               |            |
                +-------------------------------+            |
Segment +       | Number of GV slots required   | <-- the dos starts parsing 
offset * 4      | code                          |      data from here on 
                +-------------------------------+      backwards
                | First available byte for      |
                | code that does not require    |
                : the BCPL setup magic          :
                :                               :


The dos library handler startup code parses then the data BACKWARDS, starting
at the indicated longword, i.e. at the  address "Segment + Offset * 4", 
where "Offset = (Segment+4).L".

The first long word to be parsed - and hence the last long word of the 
BCPL segment - is the number of slots the dos.library setup code should
allocate.

Each entry in the table that follows, again read in backwards direction,
consists of pairs of long words. These pairs give an offset, index
information for the GlobVec entries to be defined. The first longword of the 
pair, at the higher address (remember that this table is scanned backwards!),
is the offset of the address to be put into the GlobVec, as a byte offset
from the first data byte of the hunk. This offset will, therefore, be added
to "Segment + 4" to define the data that should end up in the GlobVec. The
second member of the pair is the index into the GlobVec where this data
will be put. Since this is, BCPL-typically, a longword index, this index
has to be multiplied by four to get the byte offset from the beginning of
the GlobVec.

Only one important GlobVec entry should be mentioned here, namely GV #1
at location +4, which is the BCPL startup point.

This array of GlobVec setup information is terminated by a NULL-offset 
longword. Note that offset 0 of the hunk never contains any useful information
because it was already used to find the start of the setup table.



Here's the dos library setup code in pseudo-code: 
Brackets denote indirection, i.e. (xxx).L is "the longword at location xxx".


BCPLStartup(segment)            ;segment is a BPTR as returned by LoadSeg

    slots = 0
    WHILE segment<>0
        segment = segment * 4            ;get APTR to segment
        offset  = (segment + 4).L        ;read table offset
        table   = segment + offset       ;get the start (or end) of the setup
                                         ;information

        IF slots < (table).L THEN
            slots = (table).L            ;get the number of GV slots to be
                                         ;reserved for this program
        DO
            table = table - 4            ;next data word
            func  = (table).L            ;read the function/data offset    
            IF func=0 THEN BREAK         ;terminate the loop
            table = table - 4            ;next GV offset loop
            index = (table).L            ;read the offset information
        
            func  = func + segment + 4   ;offset from the first data byte
            (GlobVec + index * 4) = func ;define the GlobVec data
                                         ;entries are longwords, hence
                                         ;the longword index has to be 
                                         ;multiplied by four
        LOOP

        segment = (segment).L            ;get the next segment
    END


If the handler segment would be the only segment that would be used to
build the GlobVec, the GlobVec would end up mainly empty. Hence, before
running this code on your own segment, it will be run on some (currently
two) system segments in ROM which define the system default GlobVec entries.

The system functions in the GlobVec are close relatives of the functions
in the dos.library, hence no advantage can be taken by using them.
Well, possibly except for Os 1.3, but who's using this anyhow nowadays...


After execution of this code, the dos.library will start whatever it
finds in the GlobVec #1, passing in register d1 the BPTR to the DosPacket
startup structure (NOT to the message structure). Hence, *IF* this startup
mechanism must be used, you've to define at least this GV entry. 

At the end of the code, you should *NOT* run into an RTS. BCPL works
different and has a stack that grows "in the wrong way". The usual BCPL
function calls are also affected by this, and you've to jump into a 
procedure whose address is in register a6 that will remove the return 
address from the BCPL stack which is pointed to by register a1. Hence, your
code has to preserve this register, at least, and should also preserve
register a5 because this is the code that must be used to call a BCPL
procedure... even if you don't want to do that. Possibly, you should also
leave a0 blank because the original BCPL code assumed that as well. The
current dos.library implementation of the exit code does no longer require
this. Other registers have also a special meaning I don't want to document.

Hence, a minimal startup code looks like this:

    movem.l a0/a1/a5/a6,-(a7)       ;keep BCPL registers
    lsl.l #2,d1                     ;get APTR from BCPL ptr to
                                    ;startup packet
    move.l d1,a0                    ;a0 is better suited for this.
    bsr Main                        ;call the main procedure
    movem.l (a7)+,a0/a1/a5/a6       ;pop registers
    jmp (a6)                        ;run the BCPL way of saying "RTS"


iv) Examples.

Let's investigate the port handler replacement of Stephan Rupprecht as a
first example. Here's the startup code as source...

;*************************************************
;** Port-Handler Startup                        **
;** BCPL-Magic                                  **
;*************************************************
BCPLEntry    =    1                             ;GV #1: entry point
Start:
        dc.l (End-Start)/4                      ;offset to the setup table
Run:
        bra.s _BCPLInit                         ;jump to the real setup code
        nop                                     ;just to keep it LW aligned

        dc.l 0                                  ;end of the table
        dc.l BCPLEntry                          ;define GV #1
        dc.l Run-Start                          ;function offset
        dc.l 1                                  ;number of slots required
                                                ;
End:                                            ;

_BCPLInit:                                      ;this is the real init-code
        move.l a1,-(a7)                         ;push back registers
                                                ;everything else is
                                                ;preserved by the main
                                                ;entry point
        lsl.l #2,d1                             ;get DosPacket APTR
                                                ;and so on, and so on...
            :
            :
        jmp (a6)                                ;run into BCPL 
                                                ;"return from subroutine"

The FastFilingSystem uses a "special" trick: If it is run from the ROM, it
"appears" to be a BCPL handler since the dos.library sets up DF0: and DF1:
as BCPL handlers. However, if loaded from a file, it is a C handler. However,
the old BCPL magic is still in there as it is in the ROM.

Here's the binary:

0000: 000003F3 00000000 00000002 00000000    ...ó............     
0010: 00000001 000017ED 00000000 000003E9    .......í.......é     
0020: 000017ED 72006008 00000000 00000012    ...ír.`.........     
0030: 48E700FE E5892441 2F016160 221F4CDF    Hç.þå.$A/.a`".Lß     
0040: 7F004A81 66024E75 4ED64AFC 00000026    ..J.f.NuNÖJü...&     
0050: 00000050 002800AF 0000006A 00000056    ...P.(.¯...j...V     
0060: 00000004 00000000 00000001 00000004    ................     
0070: 00000096 24564552 3A206673 2034302E    ....$VER: fs 40.     

...and here the interpretation:

000003F3            HUNK_HEADER
00000000            no resident libraries in use (obsolete feature anyhow)
00000002            two segments in this binary
00000000            start loading at segment 0
00000001            end with segment 1
000017ED            length of the first segment in long words
00000000            length of the second segment in long words... it's blank
000003E9            HUNK_CODE
000017ED            number of long words to load

Up to now, this is only the data structure expected by the segment loader,
i.e. LoadSeg(). This is not part of the setup logic.

Next is the C startup. If loaded by the DOS as external handler, it will
go thru the "usual" startup and execution starts here

72006008            MOVEQ #0,d1             ;setup a blank DosPacket pointer
                                            ;to inform the startup code to
                                            ;get it manually
                    BRA.S *+8               ;jump into the startup code

00000000                                    ;This is now a special trick!
                                            ;Just the same code is used in
                                            ;the ROM, and THIS IS where
                                            ;a "faked" seglist pointer will 
                                            ;be set to. Hence, this longword
                                            ;"looks like" a NULL "next
                                            ;segment" pointer to the dos
                                            ;startup code

00000012            Offset                  ;to the begining of the BCPL
                                            ;setup data

48E700FE            movem.l a0-a6,-(a7)     ;startup code, the branch
    :                                       ;above jumps in here
    :               lsl.l    #2,d1          ;this is the BCPL startup packet
                    movea.l    d1,a2        ;or NULL on a "usual" startup
                    move.l    d1,-(a7)
                    bsr.s    *+160          ;run the main code
                    move.l    (a7)+,d1      ;pop the stack argument
                    movem.l    (a7)+,a0-a6  ;pop registers
                    tst.l    d1             ;test BCPL or C startup again
                    bne.s    *+2
                    rts                     ;on a regular startup just die.
                    jmp    (a6)             ;on a BCPL startup, run into
                                            ;BCPL "return".

and later on in the data...

00000000                                    ;end of BCPL setup data
00000001                                    ;GV #1 has to be defined
00000004                                    ;function starts at byte offset
                                            ;+4 of the hunk data, 
                                            ;this is just the procedure above
00000096                                    ;this is where the "offset 12"
                                            ;above points to. The FFS 
                                            ;indicates therefore to require
                                            ;150 slots (even though only one
                                            ;is defined).

Nice trick, what do you think? If you check where the seglist of DF0: points
to, you'll find a BPTR to the NULL long word above. However, if you check
what's in front of the NULL, its the C startup code as found in the file,
and not the segment length, as usual. It's a faked segment pointer, after
all, but good enough.

______________________________________________________________________________

References:        

[1]            Ralph Babel, The Amiga Guru Book, 2nd. Ed., Taunusstein 1993

[2,3]          Fish Disks 20 and 84.

______________________________________________________________________________

                         The THOR-Software Licence (v2, 24th June 1998)


This License applies to the documentation known as "BCPLMagic.doc".
The "Program", below, refers to this data. The "Archive" refers to the 
package of distribution, as prepared by the author of the Program, 
Thomas Richter. Each licensee is addressed as "you".



The Program and the data in the archive are freely distributable
under the restrictions stated below, but are also Copyright (c)
Thomas Richter.

Distribution of the Program, the Archive and the data in the Archive by a
commercial organization without written permission from the author to any
third party is prohibited if any payment is made in connection with such
distribution, whether directly (as in payment for a copy of the Program) or
indirectly (as in payment for some service related to the Program, or
payment for some product or service that includes a copy of the Program
"without charge"; these are only examples, and not an exhaustive enumeration
of prohibited activities).


However, the following methods of distribution
involving payment shall not in and of themselves be a violation of this
restriction:


(i) Posting the Program on a public access information storage and
retrieval service for which a fee is received for retrieving information
(such as an on-line service), provided that the fee is not
content-dependent (i.e., the fee would be the same for retrieving the same
volume of information consisting of random data).


(ii) Distributing the Program on a CD-ROM, provided that

a) the Archive is reproduced entirely and verbatim on such CD-ROM, including
especially this licence agreement;

b) the CD-ROM is made available to the public for a nominal fee only,

c) a copy of the CD is made available to the author for free except for
shipment costs, and

d) provided further that all information on such CD-ROM is redistributable
for non-commercial purposes without charge.


Redistribution of a modified version of the Archive, the Program or the
contents of the Archive is prohibited in any way, by any organization,
regardless whether commercial or non-commercial. Everything must be kept
together, in original and unmodified form.




Limitations.


THE PROGRAM IS PROVIDED TO YOU "AS IS", WITHOUT WARRANTY. THERE IS NO
WARRANTY FOR THE PROGRAM, EITHER EXPRESSED OR IMPLIED, INCLUDING, BUT NOT
LIMITED TO, THE IMPLIED WARRANTIES OF MERCHANTABILITY AND FITNESS FOR A
PARTICULAR PURPOSE AND NON-INFRINGEMENT OF THIRD PARTY RIGHTS. THE ENTIRE
RISK AS TO THE QUALITY AND PERFORMANCE OF THE PROGRAM IS WITH YOU. SHOULD
THE PROGRAM PROVE DEFECTIVE, YOU ASSUME THE COST OF ALL NECESSARY
SERVICING, REPAIR OR CORRECTION.


IF YOU DO NOT ACCEPT THIS LICENCE, YOU MUST DELETE THE PROGRAM, THE ARCHIVE
AND ALL DATA OF THIS ARCHIVE FROM YOUR STORAGE SYSTEM. YOU ACCEPT THIS
LICENCE BY USING OR REDISTRIBUTING THE PROGRAM.


                                                        Thomas Richter

______________________________________________________________________________