TABLE OF CONTENTS

ramdrive.device/CMD_CLEAR
ramdrive.device/CMD_READ
ramdrive.device/CMD_UPDATE
ramdrive.device/CMD_WRITE
ramdrive.device/KillRAD
ramdrive.device/KillRAD0
ramdrive.device/TD_CHANGENUM
ramdrive.device/TD_CHANGESTATE
ramdrive.device/TD_FORMAT
ramdrive.device/TD_GETGEOMETRY
ramdrive.device/TD_MOTOR
ramdrive.device/TD_PROTSTATUS

ramdrive.device/CMD_CLEAR                           ramdrive.device/CMD_CLEAR

   NAME
	CMD_CLEAR/ETD_CLEAR -- mark the internal buffer as containing
			       invalid data.

   FUNCTION
	As the ramdrive.device does not have an internal buffer, this
	command performs no operation. It is only implemented to be
	consistent with the trackdisk.device type of interface.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_CLEAR or ETD_CLEAR
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success.

   SEE ALSO
	CMD_WRITE, CMD_UPDATE


ramdrive.device/CMD_READ                             ramdrive.device/CMD_READ

   NAME
	CMD_READ/ETD_READ -- read data from ramdrive.

   FUNCTION
	These commands transfer data from the ramdrive to a supplied buffer.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_READ or ETD_READ
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to read
	io_Offset	byte offset from the start of the card describing
			where to read data from.

   IO REQUEST RESULT
	io_Error - 0 for success.

   NOTES

   SEE ALSO
	CMD_WRITE


ramdrive.device/CMD_UPDATE                         ramdrive.device/CMD_UPDATE

   NAME
	CMD_UPDATE/ETD_UPDATE -- write out internal buffers to ram.

   FUNCTION
	As the ramdrive.device does not buffer data internally, this
	command performs no operation and returns immediately. It is
	implemented to support file systems that use it as part of the
	regular trackdisk-type device interface.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_UPDATE or ETD_UPDATE
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success.

   SEE ALSO
	CMD_WRITE


ramdrive.device/CMD_WRITE                           ramdrive.device/CMD_WRITE

   NAME
	CMD_WRITE/ETD_WRITE -- write data to ramdrive.

   FUNCTION
	These commands transfer data from a supplied buffer to ram.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_WRITE or ETD_WRITE
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to write.
	io_Offset	byte offset from the start of the card describing
			where to write data to.

   IO REQUEST RESULT
	io_Error - 0 for success.

   NOTES

   SEE ALSO
	CMD_READ, TD_FORMAT


ramdrive.device/KillRAD                               ramdrive.device/KillRAD

   NAME
	KillRAD -- kill ramdrive.device unit

   SYNOPSIS
	devName = KillRAD(unit)

	char *KillRAD( ULONG );

   FUNCTION
	Kill a RAD: disk and return its memory.  First, remove the
	system hooks that recover the disk memory after reset, then
	free the disk memory, and return the dos device name.

   INPUTS
	unit - the unit of the ramdrive.device to kill.

   RESULTS
	devName - a pointer to the colon terminated device name that
		was associated with this unit.  This is a null
		terminated C string.


ramdrive.device/KillRAD0                             ramdrive.device/KillRAD0

   NAME
	KillRAD0 -- kill ramdrive.device unit 0

   SYNOPSIS
	devName = KillRAD(unit)

	char *KillRAD( ULONG );

   FUNCTION
	Perform a KillRAD(0).  This function is retained for
	historical reasons.

   SEE ALSO
	ramdrive.device/KillRAD


ramdrive.device/TD_CHANGENUM                     ramdrive.device/TD_CHANGENUM

   NAME
	TD_CHANGENUM -- return the current value of the counter.

   FUNCTION
	This command returns the current value of the ramdrive counter (as
	used by the enhanced commands). The change counter is always 1.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_CHANGENUM
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success.
	io_Actual - is always 1.


ramdrive.device/TD_CHANGESTATE                 ramdrive.device/TD_CHANGESTATE

   NAME
	TD_CHANGESTATE -- check if the ramdrive is currently available.

   FUNCTION
	This command checks to see if the ramdrive is available. As it
	always is, this command always returns 0.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_CHANGESTATE
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success.
	io_Actual - 0, indicating that the ram can be read from or
		    written to.


ramdrive.device/TD_FORMAT                           ramdrive.device/TD_FORMAT

   NAME
	TD_FORMAT/ETD_FORMAT -- Write data to memory

   FUNCTION
	This function is traditionally used to write data to a disk
	that has not yet been formatted before or has had a hard error
	on a standard write command. None of these states apply to the
	ramdrive.device, and as such, this command is identical to
	CMD_WRITE.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_FORMAT or ETD_FORMAT
	io_Flags	0 or IOF_QUICK
	io_Data		points to a buffer containing the data to write to the
			track, must be at least as large as io_Length.
	io_Length	number of bytes to write.
	io_Offset	byte offset from the start of the device.

   IO REQUEST RESULT
	io_Error - 0 for success.

   NOTES

   SEE ALSO
	CMD_WRITE, TD_RAWWRITE


ramdrive.device/TD_GETGEOMETRY                 ramdrive.device/TD_GETGEOMETRY

   NAME
       TD_GETGEOMETRY -- return the geometry of the ramdrive.

   FUNCTION
	This command returns a full set of information about the
	layout of the drive. The information is returned in the
	DriveGeometry structure pointed to by io_Data.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_GETGEOMETRY
	io_Flags	0 or IOF_QUICK
	io_Data		Pointer to a DriveGeometry structure
	io_Length	sizeof(struct DriveGeometry)

   IO REQUEST RESULT
	io_Error - 0 for success.

   NOTE

   SEE ALSO
	TD_GETDRIVETYPE, TD_GETNUMTRACKS


ramdrive.device/TD_MOTOR                             ramdrive.device/TD_MOTOR

   NAME
	TD_MOTOR/ETD_MOTOR -- control the on/off state of the virtual motor.

   FUNCTION
	This command would usually give control over the drive LED or
	motor of a drive. As the ramdrive does not have either, this command
	does nothing and always indicates success.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_MOTOR or ETD_MOTOR
	io_Flags	0 or IOF_QUICK
	io_Length	ignored.

   IO REQUEST RESULT
	io_Error - 0 for success
	io_Actual - always 1, indicating a running motor.


ramdrive.device/TD_PROTSTATUS                   ramdrive.device/TD_PROTSTATUS

   NAME
	TD_PROTSTATUS -- return whether the ram is write-protected.

   FUNCTION
	This command is used to determine whether the ram drive is
	currently write-protected. The write protection status can
	be set with bit 0 of the flags value of OpenDevice().

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_PROTSTATUS
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success.
	io_Actual - if io_Error is 0, this tells you whether the device
		    is write-protected. 0 means the device is NOT write-
		    protected, while any other value indicates it is.