TABLE OF CONTENTS

scsi.device/CMD_READ
scsi.device/CMD_START
scsi.device/CMD_STOP
scsi.device/CMD_UPDATE
scsi.device/CMD_WRITE
scsi.device/HD_SCSICMD
scsi.device/TD_ADDCHANGEINT
scsi.device/TD_CHANGENUM
scsi.device/TD_CHANGESTATE
scsi.device/TD_EJECT
scsi.device/TD_FORMAT
scsi.device/TD_FORMAT64
scsi.device/TD_GETGEOMETRY
scsi.device/TD_MOTOR
scsi.device/TD_PROTSTATUS
scsi.device/TD_READ64
scsi.device/TD_REMCHANGEINT
scsi.device/TD_SEEK
scsi.device/TD_SEEK64
scsi.device/TD_WRITE64

scsi.device/CMD_READ                                     scsi.device/CMD_READ

   NAME
	CMD_READ -- read sectors of data from a disk.

   FUNCTION
	This command reads data from the drive to a supplied buffer.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_READ
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to read, must be a multiple of
			the drive block size.
	io_Offset	byte offset from the start of the disk describing
			where to read data from, must be a multiple of
			the drive block size.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
   NOTES
	This command can only reach data below the 4GB barrier. To read
	data beyond the barrier, use TD_READ64 instead.

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to read more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	CMD_WRITE, TD_READ64


scsi.device/CMD_START                                   scsi.device/CMD_START

   NAME
       CMD_START -- start a drive, if possible.

   FUNCTION
	This command causes the drive to attempt spinning up the motor and
	return from an idle operation.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_START
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES
	Drives may or may not react on this command. A possible
	reaction is that a parked drive spins up its motor and is
	then ready to take read or write commands.

   BUGS


scsi.device/CMD_STOP                                     scsi.device/CMD_STOP

   NAME
       CMD_STOP -- stop a drive, if possible.

   FUNCTION
	This command causes the drive to attempt spinning down the motor,
	park the drive heads and enter an idle state.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_STOP
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES
	Drives may or may not react on this command. A possible
	reaction is that the drive spins down its motor and parks
	its drive head. A CMD_START is then required to return the
	drive into an operational stage.

   BUGS


scsi.device/CMD_UPDATE                                 scsi.device/CMD_UPDATE

   NAME
	CMD_UPDATE -- write out drive cache to the disk.

   FUNCTION
	This command may instruct the connected drive to flush its internal
	buffers to the disk, and hence complete a write operation. Whether
	the drive actually has a drive cache, and performs any operation in
	response of this command is implementation defined.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_UPDATE or ETD_UPDATE
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   SEE ALSO
	TD_WRITE64, CMD_WRITE


scsi.device/CMD_WRITE                                   scsi.device/CMD_WRITE

   NAME
	CMD_WRITE -- write sectors of data to a disk.

   FUNCTION
	This command transfer data from a supplied buffer to a disk.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_WRITE
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to write, must be a multiple of
			the disk block size.
	io_Offset	byte offset from the start of the disk describing
			where to write data to, must be a multiple of
			the disk block size.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES
	This command can only reach data below the 4GB barrier. To write
	data beyond the barrier, use TD_WRITE64 instead.

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to write more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	TD_WRITE64, CMD_READ, TD_FORMAT


scsi.device/HD_SCSICMD                                 scsi.device/HD_SCSICMD

   NAME
       HD_SCSICMD -- issue a SCSI command to the drive

   FUNCTION
	This command issues a SCSI command to the drive, bypassing the
	translation from trackdisk to SCSI commands.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	HD_SCSICMD
	io_Data		pointer to a struct SCSICmd
	io_Length	sizeof(struct SCSICmd)
	io_Flags	0 or IOF_QUICK

   SCSI COMMAND INPUT
	scsi_Data	word aligned buffer to be filled or
			transmitted during the data phase of
			the scsi command.
	scsi_Length	number of bytes to be transfered during
			the SCSI data phase
	scsi_Actual	filled upon return with the actual number
			of bytes transmitted
	scsi_Command	pointer to a word aligned buffer containing
			the bytes to be transmitted during the
			SCSI command phase. That is, this buffer
			contains the SCSI commands to be issued.
	scsi_CmdLength	number of bytes to be transmitted during
			the SCSI command phase, i.e. the byte size
			of the command.
	scsi_CmdActual	filled upon return with the actual number
			of bytes transfered during the command
			phase.
	scsi_Flags	various flags, such as:
			SCSIF_WRITE: transfer from RAM to disk
			SCSIF_READ: transfer from disk to RAM
			SCSIF_AUTOSENSE: automatically sense
			error status upon failure
	scsi_Status	returned status of the command, see
			<devices/scsidisk.h>
	scsi_SenseData	pointer to a word aligned buffer that
			is filled with sense data upon failure
			if the SCSIF_AUTOSENSE flag is set.
	scsi_SenseLength size of the autosense buffer
	scsi_SenseActual actual number of sense bytes returned

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h> or <devices/scsidisk.h>

   NOTES
	The scsi.device may actually not be connected to a SCSI
	bus at all, but may emulate (some) SCSI commands through
	appropriate IDE commands. If the connected device speaks
	ATAPI, then the SCSI commands are directly dispatched
	as ATAPI commands. Note that ATAPI uses the same command
	set as SCSI.

	However, for non-ATAPI devices, the following table lists
	which SCSI commands are emulated through ATA commands:

	READ(6)		(0x08)
	READ(10)	(0x28)
	WRITE(6)	(0x0a)
	WRITE(10)	(0x2a)
	REQUEST_SENSE	(0x03)
	FORMAT_UNIT(6)	(0x04)
	TEST_UNIT_READY	(0x00)
	SEEK(6)		(0x0b)
	SEEK(10)	(0x2b)
	READ_CAPACITY	(0x25)
	MODE_SENSE	(0x1a)
	INQUIRY		(0x12)
	REZERO_UNIT	(0x01)
	VERIFY		(0x2f)
	RESERVE		(0x16)
	SEND_DIAGNOSTIC	(0x1d)

	The following mode pages are emulated through MODE_SENSE:
	    Page 3 (Format Device page)
	    Page 4 (Rigid Disk page)
	
   BUGS


scsi.device/TD_ADDCHANGEINT                       scsi.device/TD_ADDCHANGEINT

   NAME
	TD_ADDCHANGEINT -- add a disk change software interrupt handler.

   FUNCTION
	This command lets you add a software interrupt handler to the
	scsi.device that gets invoked whenever a disk insertion or removal
	occurs.

	You must pass in a properly initialized Exec Interrupt structure
	and be prepared to deal with disk insertions/removals
	immediately. From within the interrupt handler, you may only call the
	status commands that can use IOF_QUICK.

	To set up the handler, an Interrupt structure must be initialized.
	This structure is supplied as the io_Data to the TD_ADDCHANGEINT
	command. The handler then gets linked into the handler chain and
	gets invoked whenever a disk change happens. You must eventually
	remove the handler before you exit.

	This command only returns when the handler is removed. That is,
	the device holds onto the IO request until the TD_REMCHANGEINT command
	is executed with that same IO request. Hence, you must use SendIO()
	with this command.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_ADDCHANGEINT
	io_Flags	0
	io_Length	sizeof(struct Interrupt)
	io_Data		pointer to Interrupt structure

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   SEE ALSO
	TD_REMCHANGEINT, <devices/trackdisk.h>, <exec/interrupts.h>,
	exec.library/Cause()


scsi.device/TD_CHANGENUM                             scsi.device/TD_CHANGENUM

   NAME
	TD_CHANGENUM -- return the current value of the disk-change counter.

   FUNCTION
	This command returns the current value of the disk-change counter (as
	used by the enhanced commands). The disk change counter is incremented
	each time a disk is inserted or removed from the device unit.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_CHANGENUM
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
	io_Actual - if io_Error is 0, this contains the current value of the
		    disk-change counter.


scsi.device/TD_CHANGESTATE                         scsi.device/TD_CHANGESTATE

   NAME
	TD_CHANGESTATE -- check if a disk is currently in a device unit.

   FUNCTION
	This command checks to see if there is currently a disk in a unit.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_CHANGESTATE
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
	io_Actual - if io_Error is 0, this tells you whether a disk is in
		    the drive. 0 means there is a disk, while anything else
		    indicates there is no disk.


scsi.device/TD_EJECT                                     scsi.device/TD_EJECT

   NAME
       TD_EJECT -- eject (or load) the disk in the drive, if possible.

   FUNCTION
	This command causes the drive to attempt to eject the disk in
	it, if any.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_EJECT
	io_Flags	0 or IOF_QUICK
	io_Length	0 (load, if supported) or 1 (eject)

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   BUGS


scsi.device/TD_FORMAT                                   scsi.device/TD_FORMAT

   NAME
	TD_FORMAT -- write data to disk.

   FUNCTION
	This command is traditionally used to write data to disk that
	has not yet been formatted or has had a hard error on a standard write
	command. However, as scsi and ide drives come pre-formatted, these
	commands are identical to CMD_READ.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_FORMAT
	io_Flags	0 or IOF_QUICK
	io_Data		points to a buffer containing the data to write to the
			disk, must be at least as large as io_Length.
	io_Length	number of bytes to format, must be a multiple of the
			block size of the drive.
	io_Offset	byte offset from the start of the disk for the block
			to write to, must be a multiple of the drive block size.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES
	This command can only reach data below the 4GB barrier. To write
	data beyond the barrier, use TD_FORMAT64 instead.

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to write more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	CMD_WRITE, TD_FORMAT64


scsi.device/TD_FORMAT64                               scsi.device/TD_FORMAT64

   NAME
	TD_FORMAT64 -- write data to disk, 64 bit extended

   FUNCTION
	This command is traditionally used to write data to disk that
	has not yet been formatted or has had a hard error on a standard write
	command. However, as scsi and ide drives come pre-formatted, these
	commands are identical to TD_WRITE64.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_FORMAT64
	io_Flags	0 or IOF_QUICK
	io_Data		points to a buffer containing the data to write to the
			disk, must be at least as large as io_Length.
	io_Length	number of bytes to format, must be a multiple of the
			block size of the drive.
	io_Offset	low 32 bits of the byte offset from the start of the
			disk to the block to write to.
	io_Actual	high 32 bits of the byte offset.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to write more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	TD_SEEK64


scsi.device/TD_GETGEOMETRY                         scsi.device/TD_GETGEOMETRY

   NAME
       TD_GETGEOMETRY -- return the geometry of the drive.

   FUNCTION
	This command returns a full set of information about the
	layout of the drive. The information is returned in the
	DriveGeometry structure pointed to by io_Data.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_GETGEOMETRY
	io_Flags	0 or IOF_QUICK
	io_Data		Pointer to a DriveGeometry structure
	io_Length	sizeof(struct DriveGeometry)

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTE
	This information may change when a disk in inserted when
	certain hardware is present.

	The information provided with this command may not actually
	reflect the true device geometry as hard disk geometries are
	more complex than what can be described by the DriveGeometry
	structure. However, the size of the medium described by this
	structure is "approximately correct" in the sense that the
	sector size is correct (or accepted by the drive), and the
	number of blocks due to this structure is not larger than
	the physical block count of the drive.

   SEE ALSO
	TD_GETDRIVETYPE, TD_GETNUMTRACKS


scsi.device/TD_MOTOR                                     scsi.device/TD_MOTOR

   NAME
	TD_MOTOR/ETD_MOTOR -- control the on/off state of a drive motor
	or the drive LED.	

   FUNCTION
	This command gives control over the disk motor or the drive status
	LED. The motor/motor light may be turned on or off.

	Turning the drive on is not necessary, the device does this
	automatically if it receives a request when the motor is off. Some
	drives control the drive LED automatically ignoring the TD_MOTOR
	command.

	In addition, the standard instructions to the user are that it is safe
	to remove a disk from a drive if and only if the motor is off (that is,
	if the disk light is off).

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_MOTOR or ETD_MOTOR
	io_Flags	0 or IOF_QUICK
	io_Length	the requested state of the motor, 0 to turn the motor
			off, and 1 to turn the motor on.
	iotd_Count	(ETD_MOTOR only) maximum allowable change counter
			value.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
	io_Actual - if io_Error is 0 this contains the previous state of the
		    drive motor.


scsi.device/TD_PROTSTATUS                           scsi.device/TD_PROTSTATUS

   NAME
	TD_PROTSTATUS -- return whether the current disk is write-protected.

   FUNCTION
	This command is used to determine whether the current disk is
	write-protected.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_PROTSTATUS
	io_Flags	0 or IOF_QUICK

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
	io_Actual - if io_Error is 0, this tells you whether the disk in the
		    drive is write-protected. 0 means the disk is NOT write-
		    protected, while any other value indicates it is.


scsi.device/TD_READ64                                   scsi.device/TD_READ64

   NAME
	TD_READ64 -- read sectors of data from a disk.

   FUNCTION
	This command reads data from the drive to a supplied buffer.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	CMD_READ
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to read, must be a multiple of
			the drive block size.
	io_Offset	low 32 bit of the byte offset from the start of the
			disk describing where to read data from, must be a
			multiple of the drive block size.
	io_Actual	high 32 bit of the byte offset where to read data
			from.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>
   NOTES

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to read more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	TD_WRITE64, TD_WRITE64


scsi.device/TD_REMCHANGEINT                       scsi.device/TD_REMCHANGEINT

   NAME
	TD_REMCHANGEINT -- remove a disk change software interrupt handler.

   FUNCTION
	This command removes a disk change software interrupt added
	by a previous use of TD_ADDCHANGEINT.

   IO REQUEST INPUT
	The same IO request used for TD_ADDCHANGEINT.

	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_REMCHANGEINT
	io_Flags	0
	io_Length	sizeof(struct Interrupt)
	io_Data		pointer to Interrupt structure

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   BUGS

   SEE ALSO
	TD_ADDCHANGEINT, <devices/trackdisk.h>


scsi.device/TD_SEEK                                       scsi.device/TD_SEEK

   NAME
	TD_SEEK -- control positioning of the drive heads with 64 bit offset

   FUNCTION
	This command is currently provided for internal diagnostics, disk
	repair, and head cleaning only. Drives may or may not implement
	them.

	TD_SEEK move the drive heads to the track specified. The io_Offset
	field should be set to the (byte) offset to which the seek is
	to occur. TD_SEEK may not verify their position until the next
	read. That is, they may only move the heads; they do not actually read
	any data. Actually, some drives may do nothing.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_SEEK
	io_Flags	0 or IOF_QUICK
	io_Offset	byte offset from the start of the disk describing
			where to move the head to. This shall be a multiple
			of the drive block size.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>


scsi.device/TD_SEEK64                                   scsi.device/TD_SEEK64

   NAME
	TD_SEEK64 -- control positioning of the drive heads.

   FUNCTION
	These commands are currently provided for internal diagnostics,
	disk repair, and head cleaning only. Drives may or may not implement
	them.

	TD_SEEK64 move the drive heads to the track specified. The io_Offset
	field should be set to the (byte) offset to which the seek is
	to occur. TD_SEEK64 may not verify their position until the next
	read. That is, they may only move the heads; they do not actually read
	any data. Actually, some drives may do nothing.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_SEEK
	io_Flags	0 or IOF_QUICK
	io_Offset	low 32 bits of the byte offset from the start
			of the disk describing where to move the head to.
			This shall be a multiple of the drive block size.
	io_Actual	high 32 bits of the byte offset to seek to.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>


scsi.device/TD_WRITE64                                 scsi.device/TD_WRITE64

   NAME
	CMD_WRITE -- write sectors of data to a disk, with 64 bit offset

   FUNCTION
	This command transfer data from a supplied buffer to a disk.

   IO REQUEST INPUT
	io_Device	preset by the call to OpenDevice()
	io_Unit		preset by the call to OpenDevice()
	io_Command	TD_WRITE64
	io_Flags	0 or IOF_QUICK
	io_Data		pointer to the buffer where the data should be put
	io_Length	number of bytes to write, must be a multiple of
			the disk block size.
	io_Offset	low 32 bits of the byte offset from the start of
			the disk describing where to write data to, must be
			the disk block size.
	io_Actual	high 32 bits of the byte offset.

   IO REQUEST RESULT
	io_Error - 0 for success, or an error code as defined in
	           <devices/trackdisk.h>

   NOTES

   BUGS
	Some incarnations of the scsi.device, namely those that handle
	actually IDE devices, were unable to write more than 255 blocks
	in one go. This bug has been fixed in V47.

   SEE ALSO
	TD_WRITE64, TD_READ64, TD_FORMAT64